PARCOM DECISION 85/2

PROGRAMMES AND MEASURES OF 31 DECEMBER 1985

ON LIMIT VALUES AND QUALITY OBJECTIVES FOR CADMIUM DISCHARGES

THE COMMISSION ESTABLISHED BY THE CONVENTION FOR THE PREVENTION OF MARINE POLLUTION FROM LAND-BASED SOURCES, SIGNED AT PARIS ON 4 JUNE 1974,

having regard to the provisions of the Convention, and in particular to Article 18.3 thereof,

HAS ADOPTED THE FOLLOWING PROGRAMMES AND MEASURES:

Article 1

1.	Every discharge of cadmium into the maritime area as defined in Article 3a of the Convention, or into watercourses that affect the maritime area, shall require prior authorization by the competent authority of the Contracting Party concerned. Such authorizations shall lay down emission standards for the discharge and shall be reviewed periodically.

2.	The emission standards must not exceed the limit values as set out in paragraph 3 below, except where a Contracting Party applies quality objectives in conformity with Annexes II and IV.

3.	The limit values, the time limits by which they must be complied with and the monitoring procedure for discharges are laid down in Annex I. The limit values shall normally apply at the point where waste waters containing cadmium leave the industrial plant.

When waste waters containing cadmium are treated outside the industrial plant at a treatment plant intended for the removal of cadmium, the Contracting Party concerned may permit the limit values to be applied at the point where the waste waters leave the treatment plant.

4.	Without prejudice to their obligations arising from paragraphs 1, 2 and 3 and to the provisions of the Convention, the Contracting Parties may grant authorizations for new plants only if those plants apply the standards corresponding to the best technical means available when that is necessary for the prevention and elimination of pollution.

Whatever method it adopts, where for technical reasons the intended measures do not correspond to the best technical means available, the Contracting Party shall provide the Commission with evidence in support of these reasons before any authorization. The Commission shall, at its next meeting, examine the information provided.

5.	“New plant” means:

-	an industrial plant which has become operational after the date of adoption of these programmes and measures;

-	an existing industrial plant whose cadmium-processing capacity has been substantially increased after the date of adoption of these programmes and measures.

6.	The reference method of analysis to be used in determining the presence of cadmium is given in Annex III, paragraph 1. Other methods may be used provided that the limits of detection, precision and accuracy of such methods are at least as good as those laid down in Annex III, paragraph 1. The accuracy required in the measurement of effluent flow is given in Annex III, paragraph 2.

Article 2

The Contracting Parties concerned shall monitor, within the area covered by the Convention, the aquatic environment affected by discharges. In the case of discharges affecting the waters of more than one Contracting Party, the Contracting Parties concerned shall cooperate with a view to harmonizing monitoring procedures.

Article 3

1.	The Commission shall at five-yearly intervals make a comparative assessment of the implementation of these programmes and measures by Contracting Parties on the basis of information supplied to it by them pursuant to Article17 of the Convention. The information concerned shall, in particular, comprise:

-	details of authorizations laying down emission standards for discharges of cadmium,

-	the results of information collected or inventories drawn up concerning cadmium discharged into the maritime area, and into watercourses that affect the maritime area, referred to in Article 1 paragraph 1,

-	information laid down in Annex IV, paragraph 2 for those Contracting Parties applying the quality objectives,

-	the results of the monitoring of the aquatic environment carried out in accordance with Article 2. Where appropriate, these should be submitted within the framework of under the Joint Monitoring Programme.

2.	In the event of a change in scientific knowledge relating principally to the toxicity, persistence and accumulation of cadmium in living organisms and sediments, or in the event of an improvement in the best technical means available, the Commission shall consider appropriate proposals with the aim of reinforcing, if necessary, the limit values and the quality objectives, or of establishing additional limit values and additional quality objectives.

Article 4

1.	The Contracting Parties shall implement these programmes and measures by 1 January 1986.

2.	Contracting Parties shall communicate to the Commission the text of the provisions of internal law which they adopt in the field governed by these programmes and measures.

ANNEX 1

LIMIT VALUES, TIME LIMITS BY WHICH THEY MUST BE COMPLIED WITH, AND THE PROCEDURE FOR MONITORING DISCHARGES

1.	The limit values and the time limits for the industrial sectors concerned are set out together in the table below:

| Industrial sector | Limit values which must be complied with as from | Unit of measurement |
| --- | --- | --- |
|  | 1 January 1986 | 1 January 1989 |  |
| 1. Zinc mining, lead and zinc refining, cadmium metal and non-ferrous metal industry | 0,3 | 0,23 | mg/l effluent |
| 2. Manufacture of cadmium compounds | 0,53 0,5 | 0,23 | mg/l effluent g/kg cadmium handled |
| 3. Manufacture of pigments | 0,53 0,34 | 0,23 5 | mg/l effluent g/kg cadmium handled |
| 4. Manufacture of stabilizers | 0,53 0,54 | 0,23 5 | mg/l effluent g/kg cadmium handled |
| 5. Manufacture of primary and secondary batteries | 0,53 1,54 | 0,23 5 | mg/l effluent g/kg cadmium handled |
| 6. Electroplating | 0,53 0,34 | 0,23 5 | mg/l effluent g/kg cadmium handled |
| 7. Manufacture of phosphoric acid and/or phosphatic fertilizer from phosphatic rock | - | - |  |

2.	Limit values expressed as concentrations which in principle must not be exceeded are given in the above table for the industrial sectors 2, 3, 4, 5 and 6. In no instance may limit values expressed as maximum concentrations be greater that those expressed as maximum quantities divided by water requirements per kilogram of cadmium handled. However, because the concentration of cadmium in effluents depends on the volume of water involved, which differs for different processes and plants, the limit values, expressed in terms of the quantity of cadmium discharged in relation to the quantity of mercury handled, given in the above table, must be complied with in all cases.

3.	The daily average limit values are twice the corresponding monthly average limit values given in the above table.

A monitoring procedure must be instituted to check whether the discharges comply with the emission standards which have been fixed in accordance with the limit values laid down in this Annex.

This procedure must provide for the taking and analysis of samples and for measurement of the flow of the discharge and the quantity of cadmium handled.

Should the quantity of cadmium handled be impossible to determine, the monitoring procedure may be based on the quantity of cadmium that may be used in the light of the production capacity on which the authorization was based.

5.	A sample representative of the discharge over a period of 24 hours shall be taken. The quantity of cadmium discharged over a month must be calculated on the basis of the daily quantities of cadmium discharged.

However, a simplified monitoring procedure may be instituted in the case of industrial plants which do not discharge more than 10 kilograms of cadmium per annum. In the case of industrial electroplating plants, a simplified monitoring procedure may only be instituted if the total volume of the electroplating tanks is less than 1,5 m3.

ANNEX II

QUALITY OBJECTIVES

For those Contracting Parties applying quality objectives, emission standards shall be fixed so that the appropriate quality objective or objectives from among those listed below is or are complied with in the area affected by discharges of cadmium. The competent authority shall determine the area affected in each case and shall select from among the quality objectives listed in paragraph 1 below the objective or objectives that it deems appropriate having regard to the intended use of the area affected, while taking account of the fact that the purpose of these programmes and measures is to prevent and eliminate all pollution.

1.	The following quality objectives, which will be measured sufficiently close to the point of discharge, are fixed, with the object of preventing and eliminating pollution within the meaning of Articles 1 and 4 of the Convention.

1.1	The concentration of cadmium in solution in estuary waters up to the freshwater limit affected by discharges must not exceed 5 (g/litre.

1.2	The concentration of cadmium in solution must not exceed 2,5(g/litre in waters affected by discharges as follows:

(i)	territorial waters

(ii)	waters, other than estuary waters, on the landward side of the base line from which the breadth of the territorial sea is measured and extending in the case of watercourses up to the freshwater limit.

2.	In addition to the above requirements, the results of the monitoring carried out in accordance with Article 2 must be compared with the following concentrations8:

2.1	In the case of estuary waters up to the freshwater limit, a concentration of cadmium in solution of 1 (g/litre.

2.2	A concentration of cadmium in solution of 0,5 (g/litre in the case of water as follows:

(i)	territorial waters

(ii)	waters, other than estuary waters, on the landward side of the base lines from which the breadth of the territorial sea is measured and extending in the case of watercourses up to the freshwater limit.

2.3	If these concentrations are not complied with at any one of the points on the national network, the reasons must be reported to the Commission.

3.	The concentration of cadmium in sediments and/or shellfish (mollusca and crustacea), if possible of the species Mytilus edulis, must not increase significantly with time.

4.	Where several quality objectives are applied to waters in an area, the quality of the waters must be sufficient to comply with each of those objectives.

ANNEX III

REFERENCE METHOD OF MEASUREMENT

1.	The reference method of analysis used for determining the cadmium content of waters, sediment and shellfish (mollusca and crustacea) is atomic absorption spectrophotometry after preservation and suitable treatment of the sample.

The limits of detection must be such that the cadmium concentration can be measured to an accuracy of ± 30% and a precision of ± 30% at the following concentrations:

-	in the case of discharges, one-tenth of the maximum permitted concentration of cadmium specified in the authorization;

-	in the case of surface water, 0,1 (g/litre or one-tenth of the cadmium concentration specified in the quality objective, whichever is the greater;

-	in the case of shellfish (mollusca and crustacea), 0,1 mg/kg wet weight;

-	in the case of sediments, one-tenth of the cadmium concentration in the sample or 0,1 mg/kg dry weight, with drying being carried out between 105 and 110(C at constant weight, whichever value is the greater.

2.	Flow measurement must be carried out to an accuracy of ± 20%.

ANNEX IV

MONITORING PROCEDURE FOR QUALITY OBJECTIVES

1.	For each authorization the competent authority shall specify the restrictions, monitoring procedure and time limits for ensuring compliance with the quality objective(s) concerned.

2.	The Contracting Parties shall, for each quality objective chosen and applied, report to the Commission on:

-	the points of discharge and the means of dispersal,

-	the area in which the quality objective is applied,

-	the location of sampling points,

-	the frequency of sampling,

-	the methods of sampling and measurement,

-	the results obtained.

3.	Samples must be sufficiently representative of the quality of the aquatic environment in the area affected by the discharges, and the frequency of sampling must be sufficient to show any changes in the aquatic environment, taking into account, in particular, natural variations in the hydrological regime.

CADMIUM

1.	At its Sixth Meeting (Oslo, 1984), the Commission reviewed the work of the Working Group on Cadmium Pollution and adopted a number of recommendations (PARCOM 6/13/1, § 4.20 - 4.23) which are set out below.

2.	The Commission agreed that, in taking measures to eliminate pollution of Convention waters by cadmium, Contracting Parties should take into account the scope which exists for the substitution of cadmium by other materials particularly in the fields of electroplating, pigments and stabilizers. The Commission recalled that the possibility of regulating the composition of products and the use of substances is one of the “measures” envisaged by Article 4 of the Convention.

3.	The Commission agreed that the Contracting Parties should report periodically on their national schemes for labelling, collecting and recycling cadmium batteries, together with the results achieved. It was also agreed that Contracting Parties should encourage research into less harmful substitutes for cadmium in batteries.

4.	The Commission agreed that the risks resulting from the use of cadmium in soldering and alloys were a problem, although some alternatives to cadmium exist.

5.	Concerning the application of fertilizers on land, the Commission accepted that in the long-term it was likely that a certain amount of this cadmium would reach Convention waters. The Commission agreed that it would be premature to take a decision but it was agreed that further research to define the pathways and reduce the cadmium content in fertilizers should be encouraged.

*     *     *

6.	Following discussion at its Seventh Meeting (Brussels, 1985), the Commission decided to adopt by written vote, in accordance with Rule 11.6 of the Commission’s Rules of Procedure, PARCOM Decision 85/2 on limit values and quality objectives for cadmium discharges. Written votes in favour of the Decision were cast by the European Economic Community (on behalf of Belgium, Denmark, France, the Federal Republic of Germany, Ireland, the Netherlands and the United Kingdom) and by Iceland, Norway, Portugal and Sweden. Spain informed the Commission at its Sixth Meeting (Madrid, 1986) that it was able to vote in favour of the Decision (PARCOM 8/12/1, § 4.2), with the result that acceptance of PARCOM Decision 85/2 is unanimous. A copy is at Annex 1.

*     *     *

7.	At its Tenth Meeting (Lisbon, 1988), the Commission adopted a strategy for a future work programme for cadmium (PARCOM 10/10/1, § 3.15 and Annex 8). A copy is at Annex 2.

# Footnotes

Limit values for industrial sectors not mentioned in this table will, if necessary, be fixed by the Commission at a later stage. In the meantime the Contracting Parties will fix standards for cadmium discharges autonomously in accordance with Article 4.2 of the Convention. Such standards must take into account the best technical means available and must not be less stringent than the most nearly comparable limit value in this Annex.

On the basis of the experience gained in the implementation of these programmes and measures, and pursuant to Article 4.2, the Commission shall in due course consider proposals for fixing more restrictive limit values.

Monthly flow-weighted average concentration of total cadmium.

Monthly average.

It is impossible for the moment to fix limit values expressed as load. If need be, these values will be fixed by the Commission in accordance with Article 3.2 of the programmes and measures. If the Commission does not fix any limit values, the values expressed as load given in Column ‘1 January 1986’ will be kept.

Contracting Parties may suspend application of the limit values until 1 January 1989 in the case of plants which discharge less than 10 kg of cadmium a year and in which the total volume of the electroplating tanks is less than 1,5 m3, if technical or administrative considerations make such a step absolutely necessary.

At present there are no economically feasible technical methods for systematically extracting cadmium from discharges arising from the production of phosphoric acid and/or phosphatic fertilizers from phosphatic rock. No limit values have therefore been fixed for such discharges. The absence of such limit values does not release the Contracting Parties from the obligation under Article 1, paragraph 1 of these programmes and measures to fix emission standards for these discharges. Limit values will, as necessary, be fixed by the Commission at a later stage.

All concentrations relate to the arithmetic mean of the results obtained over one year.

A quality objective for the high seas is not fixed on the understanding that the quality objective for territorial waters and other waters will protect the high seas from pollution.