# ANNEX 15

(Ref: § 7.19)

# OSLO AND PARIS CONVENTIONS FOR THE PREVENTION OF MARINE POLLUTION

PROGRAMMES AND MEASURES COMMITTEE (PRAM)

# OVIEDO: 20-24 FEBRUARY 1995

# PARCOM Guidelines for Calculating Mineral Balances

# Introduction

PARCOM 1988 agreed on PARCOM Recommendation 88/2 on the Reduction of Nutrients to the Convention Area. It was agreed to achieve a substantial reduction (of the order of 50%) in inputs of phosphorus and nitrogen between 1985 and 1995 into areas where these inputs are likely, directly or indirectly to cause eutrophication.

There is a lack of appropriate direct measurements in order to evaluate whether progress is made in the reduction of emissions from agriculture to the maritime area. Furthermore the timelag between the application of measures and their effects on inputs to the maritime area is a complicating factor to evaluate the progress made.

In order to assess the effectiveness of the nutrient reduction measures taken within the agricultural sector the Paris Commission considers the evaluation of mineral balances a helpfull tool.

The frequent calculation of a national (or where appropriate regional) agricultural nutrient balance on nitrogen and phosphorus provides an estimate of overall surplus from agricultural production. The surplus contains all losses to the environment in any form. The changes over the years of the surplus can provide an overall estimate of the effects obtained by the measures taken. For comparison of the progress achieved in the different Contracting Parties a common basis for calculation is needed. The method described below makes, where possible, reference to the data reported to the EC (Eurostat).

In the second part a description of a more detailed mineral balance is given, in which it is possible to countercheck parts of the more general balance.

# Calculation of the basic national mineral balance

The basic national mineral balance for phosphorus (P) and nitrogen (N) is presented as a flow chart in Figure 1. The agricultural production system is essentially considered to be a "black box", and only data for INPUT (import from abroad and other sectors) and OUTPUT (export of agricultural products and consumption) have to be provided; the SURPLUS is calculated as the difference between these two.

Figure 1

In formula (for N and P):

# AGRICULTURAL SURPLUS = INPUT - OUTPUT

# INPUT:

# IMPORT FEED

# FODDER PHOSPATE

CHEMICAL FERTILIZER

OTHER INPUTS (return from food industry, sewage sludge, N-binding)

DEPOSITION (for nitrogen exclusive NH3-emissions from agriculture that returns)

# OUTPUT:

INDUSTRY (FOOD and NON-FOOD)

# FARM SALES OF AGRICULTURAL PRODUCTS

# EXPORT FODDERS

EXPORT (UNPROCESSED) AGRICULTURAL PRODUCTS

Source of data

Most quantitative data for the calculation are obtained from national economic statistics, which are reported annually to Eurostat, the statistical office of the EC (for EC-members; EFTA-countries have a similar annual report). Countries are advised to contact their statistical institutes to obtain these data. If necessary, most data can be obtained from the references mentioned (Eurostat 5A-Agriculture, 6C-Foreign trade; OECD food consumption statistics; FAO Statistics 102-Trade, 104-Production, 106-Fertilizers).

Data of nitrogen and phosphorus contents in products are obtained from analysis of manufacturers/importers (actual figures), agricultural and environmental research institutes (measurements and estimates), or, only if no other source available, estimates from literature. See Appendix 1.

The use of the most recent and accurate nutrient contents in products involved is essential for obtaining reliable balances. With changing supply and demands from e.g. the market of feed resources and animal feed industry, the (average) mineral contents in imported feed compounds may change drastically. However, the average contents of minerals and the variation therein that can be expected, depending on source and country of origin, is well known for most raw materials. Depending of country of origin and treatment given for most compounds a reliable estimate can be made.

# The complete national mineral balance

The complete national mineral balance is presented as a flow chart in Figure 2. It can be considered an expansion of Figure 1, to which an internal agricultural balance is added. This added (sub)balance can be utilised for control purposes, but is not needed for the calculation of the basic balance. However, it is worthwhile to add this information, because of the relative ease of calculation, and the countercheck this can provide on the basic balance. The required data are presented in Appendix 2.

In addition, several data on nutrient content are required. eg., in manure (ex-animal, ex-storage), in roughage, in animal etc. These contents may vary considerably between (and within) countries, depending on housing type, feeding regimes, animal genetics and production levels, abatements measures taken, etc. Therefore year-to-year estimates per country (region) should be made. It should be stressed, however, that these estimates affect the internal balance only; not the basic balance as described above.

Several checks on the accuracy of the data can be established. eg., comparison of data presented as INPUT for food industry versus data provided as OUTPUT from agriculture to industry. But more interestingly: - measured and/or estimated environmental losses (NO3, NH3, phosphate leaching) indicated as Surplus-2, versus the overall SURPLUS. Year-to-year changes in the overall surplus can easily be detected, and can be traced to their source.

Figure 2

### Summarising

• 	The basic mineral balance as described can easily be calculated for all Contracting Parties, using already available data, either from national institutes or, in many cases, international statistics.

• 	If appropriate, a comparable regional balance can be calculated similarly. Data therefore will probably be available in national statistical institutes.

• 	The comparison of year-to-year data of the basic balance can provide an accurate estimate of the effectiveness of total reduction measures taken in the agricultural sector as a whole; particularly since only anthropogenic activities are involved, and no retention time influences data.

• 	The more detailed mineral balance sheet described in the second part can probably be calculated for most Contracting Parties, using already available data.

• 	The more detailed mineral balance sheet provides several counterchecks and insight in location of losses.

# References

• 	Eurostat Series A: Statistical yearbooks, Theme 5: Agriculture, forestry and fisheries.

• 	Eurostat Series C: Accounts, surveys and statistics, Theme 6: Foreign trade, Chapters 1-24: Agriculture and foodstuffs.

• 	OECD - Food consumption statistics (by year).

• 	FAO - Statistics No. 102: Trade (yearbook)

• 	FAO - Statistics No. 104: Production (yearbook)

• 	FAO - Statistics No. 102: Fertilizer (yearbook)

• 	PARCOM Emission Factors Manual

# Appendix 1

# Data for the basic balance sheet are obtained as follows (see figure 2):

| BASIC MINERAL BALANCE | Source composition data | Source quantitative data | Reference |
| --- | --- | --- | --- |
| INPUT |  |  |  |
| • Import feed |  |  |  |
| Import concentrate (compounds) | AR, IND | IT, IND | EC, OECD, FAO |
| Import roughage (grass-silage, maize) | AR | IT | EC, OECD, FAO |
| • Fodder phosphate |  |  |  |
| Import fodder phosphate | IND, AR | IT, IND |  |
| Input phosphate industry | IND | IND |  |
| • Chemical fertilizer |  |  |  |
| Import chemical fertilizer | IND, (AR) | IT, IND | FAO |
| Input from fertilizer industry | IND, (AR) | IND, NT | FAO |
| • Other inputs |  |  |  |
| Returns from food industry | AR, IND | NT, AG |  |
| Sewage sludge1) | AR | NT, AG |  |
| Organic (household) waste1) | AR | NT, AG |  |
| Animal manure imports | AR | IT, AG2) |  |
| N-binding papillonaceae | AR | AG |  |
| • Deposition |  |  |  |
| Deposition by air mainly NH3 and other N- deposition (including border crossing imports, excluding NH3 remaining within agriculture) |  | ER | EMEP, Atmos |
| OUTPUT |  |  |  |
| • Industry |  |  |  |
| Products delivered to food and non-food processing industry (for national use and export) | AR, IND | NT, IND, AG | - |
| • Farm-sales agricultural products |  |  |  |
| On farm sales agricultural products for human consumption | AR, IND | NT, AG | - |
| • Export fodders |  |  |  |
| Export raw and processed fodders for animal production | AR, IND | IT, IND, AG | EC, OECD, FAO |
| • Export agricultural products |  |  |  |
| Export unprocessed agricultural products | AR, IND | IT, IND, AG | EC, OECD, FAO |

Information provided by: 		AR	Agricultural Research institutes

AG	Agricultural Statistics

ER	Environmental Research institutes

ES	Environmental Statistics

IND	Industry

IT	International Trade statistics

NT	National Trade statistics

1)	Analysis of composition by certified laboratories and registration obliged for producers and users per 1/1/93 in the Netherlands.

2)	Registration for users is mandatory in the Netherlands.

# Appendix 2

Complete mineral balance sheet: in addition to the "Basic balance" data the following information is required (see figure 2)

| COMPLETE MINERAL BALANCE | Source composition data | Source quantitative data | Reference |
| --- | --- | --- | --- |
| AGRICULTURE |  |  |  |
| • Fodder |  |  |  |
| Total fodder production, and consumption in animal production | AR | AG, NT | (EC, OECD, FAO) |
| • Excretion |  |  |  |
| Total excretion from animal production | AR | AG, (NT) |  |
| losses (NH3) | AR, ER | AG, ES |  |
| • Manure |  |  |  |
| Total manure application to field | AR | AG |  |
| losses (NH3 + NO3 + P + K) | AR, ER | AG, ES |  |
| • Farmland |  |  |  |
| Total application of fertilizer | AR | AG, (NT) |  |
| • Crop |  |  |  |
| Total harvested product; losses returning as "fertilizer" | AR, IND | AG, NT | EC ,OECD, FAO |
| • Animal products |  |  |  |
| Primary production: Meat, milk, etc. | AR, IND | AG, NT | EC, OECD, FAO |
| SURPLUS |  |  |  |
| • Overall SURPLUS |  |  |  |
| calculated as mentioned in table 1 | * | * |  |
| • SURPLUS-2 |  |  |  |
| Detailed surplus from known loss sources e.g. NH3, NO3 measurements, etc. | AR, ER | AG, ES |  |

Information provided by:	AR	Agricultural Research institutes

AG	Agricultural Statistics

ER	Environmental Research institutes

ES	Environmental Statistics

IND	Industry

IT	International Trade statistics

NT	National Trade statistics

# Footnotes

This may include both public and confidentially provided information available in Statistical offices.

This may include both incidental and frequently updated research;

eg., a continually updated table with composition of all available feedstuffs is available from the Dutch "Central Bureau of Feedstuffs".

Data used in these calculation will be available in most countries.

# Text boxes

OUTPUT

Deposition

Other inputs

Chemical fertilizer

Fodder phosphate

Import feed

# Agriculture

INPUT

Export (unprocesssed) agricultural products

Export fodders

Farm sales of agricultural products

Industry (food and non-food)

# Agriculture

SURPLUS

Deposition

Other
Inputs

Chemical
fertilizer

Fodder
phosphate

Import
feed

SURPLUS

INPUT

Export Agricultural
products

Export
fodders

Farm-sale Agricultural products

Industry
Food & Non-food

OUTPUT

Fodder

Excretion

Animal
products

Manure

Farmland

Crop

Surplus-2