EIHA 14/10/1, Annex 15

Impulsive noise monitoring reporting format

Agreement 2014-10

Impulsive Noise Register – Reporting Format Note

| Column Header | Format Example | Explanation |
| --- | --- | --- |
| Minimum / Essential information |
| Country | Belgium | The country where the source was registered |
| CP_ID | BE001 | An identifier which is unique to the country and the data entry point (i.e. the first entry may be 1, the second 2 etc |
| Date | 20130327 | The date of the detection in YYYYMMDD format |

| Data should either be reported as Latitude, Longitude, Source_Level_Point: |
| --- |
| Latitude (point source) | 51,3683 | The latitude of the detection in decimal degrees, using WGS84 |
| Longitude (point source) | 2,6733 | The longitude of the detection in decimal degrees, using WGS84 |
| Source_Level_Point | Airgun | One of the thresholds below should be chosen based on the source and duration of the event: |
|  |  | Explosive | mTNTeq > 8 g |
|  |  | Airgun | SLz-p >209 dB re 1μPa m |
|  |  | Other pulse sound source | SLE >186 dB re 1μPa2m2s |
|  |  | Low-mid frequency sonar | SL > 176 dB re 1 μPa m |
|  |  | Low-mid frequency acoustic deterrent | SL > 176 dB re 1 μPa m |
|  |  | Other non-pulse sound source | SL > 176 dB re 1 μPa m |

| OR if point data is not available, it can be submitted as bins; provided the bins (e.g. licence blocks) are also provided as spatial data: |
| --- |
| Unique_ID (block) | 98/11 | An identifier which is unique to the block |
| Source_Level_Bin | 3 Low | If a point source level is not recorded and the operator is reporting in bins, one of the thresholds below should be chosen based on the level: |
|  |  | 1. Sonar or acoustic deterrents: |
|  |  | 1 Very low | 176-200 dB re 1 μPa m |
|  |  | 1 Low | 201-210 dB re 1 μPa m |
|  |  | 1 Medium | 211-220 dB re 1 μPa m |
|  |  | 1 High | 220 dB re 1 μPa m and above |
|  |  | 2. Generic explicitly impulsive source: |
|  |  | 2 Very low | 186-210 dB re 1 μPa2 m2s |
|  |  | 2 Low | 211-220 dB re 1 μPa2 m2s |
|  |  | 2 Medium | 221-230 dB re 1 μPa2 m2s |
|  |  | 2 High | 230 dB re 1 μPa2 m2s and above |
|  |  | 3. Airgun arrays: |
|  |  | 3 Very low | 209-233 dB re 1 μPa m |
|  |  | 3 Low | 234-243 dB re 1 μPa m |
|  |  | 3 Medium | 244-253 dB re 1 μPa m |
|  |  | 3 High | 253 dB re 1 μPa m |
|  |  | 4. Explosions |
|  |  | 4 Very low | 8g – 210g |
|  |  | 4 Low | 220g – 2,1kg |
|  |  | 4 Medium | 2,11kg – 21kg |
|  |  | 4 High | 22kg – 210kg |
|  |  | 4 Very high | 210kg and above |
|  |  | 5. Impact pile driver: |
|  |  | 5 Very low | <280kJ |
|  |  | 5 Low | 290kJ – 2,8MJ |
|  |  | 5 Medium | 2,81MJ – 28MJ |
|  |  | 5 High | >28MJ |

| The following data is optional and outlined in grey in the Excel reporting format |
| --- |
| Optional |
| Source_Spectra |  | The frequency band of the event (format to be determined) |
| Duty_Cycle |  | The percentage of the duration the signal was active (definition to be expanded) |
| Time | 13:52 | Start time of the event transmission (definition to be expanded) |
| Duration |  | The duration of the event in seconds (definition to be expanded) |
| Directivity |  | A Q value representing the directivity of the sound source (definition to be expanded) |
| Source_Depth | 5 | Approximate depth, in metres, of the sound source |
| Platform_Speed |  | Speed of the platform recording the event (definition to be expanded) |
| Remarks |  | Any free text comments or additional supporting information |