5.48	The Commission adopted PARCOM Recommendation 87/2 on discharges from reception facilities and oil terminals (Annex 11). It was also agreed that the Working Group on Oil Pollution would review its implementation in 1989.

PARCOM RECOMMENDATION 87/2

OF 3 JUNE 1987

ON DISCHARGES FROM RECEPTION FACILITIES

AND OIL TERMINALS

Contracting Parties are recommended to apply the following standard to discharges from oily waste reception facilities and oil terminals:

1.	A standard of 15 mg/1 for discharges of oily mixtures from oily waste

reception facilities and ballast treatment facilities at oil terminals.

2.	The standard will be deemed to have been met if the arithmetic mean of the oil

concentration in 5 consecutive 2 hour samples is less than 15 mg/1, measured

according to methods of sampling and analysis defined by the Working Group

on Oil Pollution. Alternative standards will be acceptable provided that the

associated methods of sampling and analysis are approved by the Working

Group on Oil Pollution as being equivalent to, or more stringent than, the Paris

Commission standard and its associated methods of sampling and analysis.

3.	The following two categories of reception facilities and oil terminals are

exempt from the standard:

(a)	reception facilities or oil terminals associated with a refinery complex;

(b)	reception facilities receiving only oily slops and oily waste water and

discharging, after gravity treatment, less than 5 tonnes of oil per annum.

4.	Contracting Parties shall report on the measures which they have taken to

implement this Recommendation at the Working Group’s Thirteenth Meeting

in 1989.