ANNEX 6

(Ref. §3.21)

OSLO AND PARIS CONVENTIONS FOR THE PREVENTION OF MARINE POLLUTION

SIXTEENTH JOINT MEETING OF THE OSLO AND PARIS COMMISSIONS

KARLSKRONA: 13-17 JUNE 1994

PARCOM Recommendation 94/2

on Best Available Techniques

and Best Environmental Practice

for the Integrated and Non-Integrated

Sulphite Paper Pulp Industry

Contracting Parties to the Convention for the Prevention of Marine Pollution from Land-Based Sources RECOMMEND that:

Best Available Techniques (BAT) and Best Environmental Practice (BEP) for the Sulphite Paper Pulp Industry include the following or equally effective measures:

1.	Dry debarking with minor waste water discharges.

2.	Closed screening.

3.	Neutralising of weak liquor before evaporation followed by re-use of most condensates in the process.

4.	Systems which enable the recovery of almost all organic substances dissolved out in the cook (a total U-value of  about 98% is achievable).

5.	No discharge from the bleach plant when the sodium based processes are being used.

6.	Secondary treatment for waste water discharges.

7.	Reduction of SO2-emissions from the recovery boiler e.g. by installing four scrubbers (a reduction of more than 99% is achievable).

8.	Reduction of NOx-emissions from the recovery boiler and auxiliary boilers e.g. by using non-catalytic reduction or by making changes in combustion techniques.

9.	For all chemical products used knowledge should be available about chemical composition, health risks for man, toxicity to aquatic organisms, rate of chemical and biological degradation and potential for bioaccumulation.

10.	The principle of substitution should be followed.  This principle means that if there is a choice between different products the one which is less hazardous to man and the environment should be used.

A Description of BAT and BEP for the Sulphite Paper Pulp Industry can be found in OSPAR 1994, Industrial Sectors: Best Available Techniques and Best Environmental Practice.

First progress report on implementation to be made to OSPAR 1997.

# Footnotes

The question of the use of molecular chlorine is dealt with in PARCOM Decision 92/1 on the Reduction of Discharges of Chlorinated Organic Substances from the Production of  Bleached Kraft and Sulphite Pulp

U-value = The proportion of the organic substances dissolved out in the cook and thereafter recovered and burned in the recovery boiler.