PARCOM  DECISION  92/1

ON  THE  REDUCTION  OF  DISCHARGES  OF  CHLORINATED

ORGANIC  SUBSTANCES  FROM  THE  PRODUCTION

OF  BLEACHED  KRAFT  AND  SULPHITE  PULP*

CONTRACTING PARTIES TO THE CONVENTION FOR THE PREVENTION OF MARINE POLLUTION FROM LAND-BASED SOURCES AGREE THAT:

1.	The discharges of chlorinated organic substances should not, as an annual average for each mill, exceed 1 kg of AOX/tonne air-dry bleached kraft or sulphite pulp.

The annual averages should, as a minimum, be based on one analysis a month.  Analysis should be made on representative, unsettled samples using DIN 39409, part 14 or SCAN-W 9:89 or other methods which should be agreed by the Commission.

2.	For new installations or existing installations subject to a substantial increase of production capacity, or subject to retrofitting, the formation of polychlorinated organic substances should be reduced by using a molecular chlorine multiple below 0,05 (ie. per tonne of pulp less than 0,5 kg of molecular chlorine, Cl2, per kappa number of pulp entering the bleach plant).  For existing installations not subject to a substantial increase of production capacity or not subject to retrofitting, this value should preferably be below 0,05 and should in any case not exceed 0,15.

3.	The objectives under 1. and 2. shall apply to all mills starting to operate on or after 1 January 1993.  For mills in operation before 1 January 1993 these objectives shall be attained by 1 January 1996.

4.	This Decision supersedes PARCOM Decision 90/1.

# Footnotes

* Reservation from Finland