ANNEX 6

(Ref. § 4.15)

OSLO AND PARIS CONVENTIONS FOR THE PREVENTION OF MARINE POLLUTION

FIFTEENTH MEETING OF THE OSLO AND PARIS COMMISSIONS

BERLIN: 14-19 JUNE 1993

________________________________________________________________________________

PARCOM RECOMMENDATION 93/1

CONCERNING LIMITATION OF POLLUTION

FROM EXISTING PRIMARY IRON AND STEEL

PRODUCTION INSTALLATIONS*

RECALLING PARCOM Recommendation 91/2 on the definition of BAT in the primary iron and steel industry

RECALLING PARCOM Recommendation 92/2 concerning the limitation of pollution from new primary iron and steel installations

Contracting Parties to the Convention for the Prevention of Marine Pollution from Land-Based Sources RECOMMEND that:

The recommendation applies for existing primary iron and steel production installations that have been granted a building licence before 1 January 1993.  The regulations in the recommendation are to come into force as from 1 January 2000.  The scope and definitions are further elaborated in a technical annex. The recommendation contains two general requirements. For processes where this general approach should be either specified or modified, separate requirements are given.

A.	General requirements

1.	Waste gases containing dust should be collected and be subjected to dedusting. After dedusting, the gases should not contain more than 50 mg dust/m3. If the dust contains hazardous substances (e.g. heavy metals such as cadmium, lead and/or chromium) lower standards should be achieved. 1, 2

2.	Water used for scrubbing, for instance for the removal of dust, HF, SO2 and NOx and rinsing purposes should be subject to recirculation. The bleed from these recirculation systems, as well as storm water, should not contain more than 35 mg suspended solids/l before discharge. Where possible, discharges should be avoided by using dry operations, e.g. for cleaning purposes.

B.	Sinter plants

3.	Sintering flue gas dust emissions should not exceed 100 mg/m3 (corresponding to 200 g/tonne sinter).

C.	Coke plants

4.	During charging, visible emissions should not occur during more than 10% of the charging period. Considerable clouds of dust or vapour (about 20-40% opacity) should not be present at any time.

5.	During coking, clouds of vapour should not be visible at more than:

a.	2% of charging hole lids.

b.	2% of ascension pipes.

c.	10% of doors.

6.	If dry quenching of cokes is applied dust sources should be enclosed and extracted (with subsequent fabric filtration or equally effective methods). Dust emissions should not exceed 20 mg/m3 (20 g/t coke). If wet quenching is applied grit arresters should be present in the quench tower.

7.	Waste water from coke oven gas treatment should comply with the following limit values: 3

|  | SUBSTANCE | CONCENTRATION |
| --- | --- | --- |
|  | Total-N | 100 mg/l | 30 g/t coal at 10% water content |
|  | COD | 200 mg/l | 120 g/t coal at 10% water content |
|  | Phenol | 0,5 mg/l | 0,15 g/t coal at 10% water content |

D.	Blast furnaces

8.	All waste gases containing dust should be collected and be subjected to dedusting. This in particular stands for gases from tapping, from pig iron desulphurisation and from charging except for top gas leakage.

9.	Waste water discharges should be minimized.

_______________________

3	The PAH content of the effluent should also be controlled, preferably to a concentration of less than 0,1 mg/l (0,03 g/t coal at 10% water content).

E.	Basic Oxygen Furnaces

10.	Primary gases from basic oxygen furnaces should not contain more than 50 mg dust/m3. As an exception this may be exceeded, but in no case should it exceed 80 mg dust/m3. The need for this exception shall be reviewed before the end of 1997.

11.	All waste gases containing dust should be collected and be subjected to dedusting. This in particular stands for gases from pig iron decanting, charging, tapping, refining (ladle metallurgy) and desulphurisation.

Technical Annex

a.	This draft Recommendation covers emissions from various processes within the primary iron and steel industry, viz. sintering, pelletizing, coking, ironmaking (in blast furnaces) and steelmaking (in basic oxygen furnaces) both in combination and stand-alone.  Emissions from related processes such as continuous casting and rolling will be covered by a separate Recommendation addressed as "secondary iron and steel production".  Electroplating operations will also be addressed by a separate Recommendation.

b.	For atmospheric emissions concentrations are expressed as mg/m3, where m3 is defined as 1 m3 of dry gas at 0°C and 1,013 x 105 MPa.

c.	Representative sampling types should be used, such as:

i.	0,5-hour average for parameters in gases;

ii.	daily average for all parameters in water;

or equally representative methods including continuous measurement.

d.	When comparing actual figures with the standards given in this document, non-compliance should be taken to occur whenever one or more individual test results, after subtracting the measuring uncertainty, exceeds the standards.

e.	If possible, the performance is related to the actual production of the process considered in g per metric tonne. "g/tonne" refers to year-based emissions.

f.	In order to quantify fugitive coke oven emissions, the term "opacity" is used.  Opacity is defined as the extent of loss of sight of the scene behind a cloud of dust as close to the source as possible.  Zero % opacity corresponds to 100% visibility of the background scene, whereas 100% opacity marks total loss of sight. A suitable example of such a method is the EPA method No.9 for opacity reading (Federal Register Vol. 39, No. 219, 12 Nov. 1974, p. 39875).

g.	In spite of their potential large environmental effects, neither process failures nor other temporary malfunctioning of installations are included by the standards presented.  In other words, the figures refer to "normal" operations.

# Footnotes

*	Belgium and Spain have a reservation on this PARCOM Recommendation. Spain lifted its reservation in 2003.

1 	Levels of dust in the order of 10 mg/m3 can be achieved by the use of fabric filters.

2 	E.g. levels of cadmium of more than 0,2% or levels of other heavy metals of more than 10% (except for iron).