Intra North Sea Ballast Water Exchange Areas

(OSPAR Agreement 2014-11)

OSPAR 2014 agreed to endorse the intra North Sea Ballast Water Exchange areas, as outlined below which have been developed by the North Sea countries (OSPAR 14/21/1, paragraph 3.7).

# Purpose

1	This Agreement designates areas in which ballast water exchange cannot take place in the North Sea for intra North Sea traffic, in accordance with the International Convention for the Control and Management of Ships Ballast Water and Sediments (the Convention). A ship on a voyage between two North Sea ports, which must at least meet the standards described in regulation D-1 of the Convention, may conduct ballast water exchange in these areas. Within Norwegian territorial waters and economic zone the Norwegian national regulation applies. This designation of areas of ballast water exchange in the North Sea is a temporary regulation. It enters into force when the Convention enters into force, and terminates when ships shall meet regulation D-2 of the Convention (ultimately 2016 for all categories of ships).

# Introduction

2	The Convention aims “to prevent, minimize and ultimately eliminate the risks to the environment, human health, property and resources arising from the transfer of Harmful Aquatic Organisms and Pathogens through the control and management of ships’ Ballast Water and Sediments, as well as to avoid unwanted side-effects from that control and to encourage developments in related knowledge and technology.”

3	Regulation B-3 of the Convention states for different categories of ships when Ballast Water Management must be conducted to at least meeting the standard described in regulation D-1: “Ballast water Exchange Standard”.

4	Regulation B-4.2 of the Convention allows ports States to designate areas, in consultation with adjacent or other States, as appropriate, where ships may conduct ballast water exchange. Regulation B-4.2 determines that such sea areas can be designated in sea areas where the distance from the nearest land or the depth does not meet the parameters described in paragraph 1.1 or 1.2 of the regulation. The North Sea falls under this category, as the required depth is to shallow.

5	The identification, assessment and designation of these areas were done taking into account the relevant guideline of the Convention: “Guidelines on Designation of Areas for Ballast Water Exchange (G14).”

6	The assessment of identified areas was done in the European Space Agency (ESA) Due Innovator II project. The goal of this project was to investigate the opportunity for remote sensing data to contribute to the risk assessment of Ballast Water exchange. Some of the basic principles used were:

  - clear water indicates a low risk

  - high chlorophyll concentration indicates high risk

  - a close distance to the coast indicates a high risk

  - low depth indicates a high risk

After careful consideration, the group proposed that ballast water exchange should, in principle, be avoided in areas with a risk index of 0,75 and above; consequently areas with a risk index lower than 0,75 can be designated as ballast water exchange areas. However, while the group agreed that a high standard of protection was desirable, taking into consideration regulation B-4 of the BWMC, the group agreed that a delay of the voyage of a deviation from the intended voyage should be avoided. The group noted that options for exchange on the Traffic Separations Scheme Terschelling-German Bight might not be sufficient with the proposed index value of 0,75. Rather than lowering the standard of protection for the North Sea as a whole, the group agreed to adjust the boundary of the designated ballast water exchange area around the TSS, in order to afford ships bound on the TSS the opportunity for ballast water exchange.

Norway has implemented parts of the Ballast Water Management Convention (D-1; Exchange standard) in its national regulations. The Norwegian Ballast Water Regulation entered into force on 1 July 2010. As regulation B-4.2 in the BWMC allows, Norway has designated areas for ballast water exchange within its exclusive economic zone (EEZ). Areas within Norway´s EEZ are therefore excluded from the current proposal. The Norwegian ballast water exchange areas are displayed in Annex 2.

7	The North Sea area means the North Sea proper including seas therein with the boundary between:

.1	the North Sea southwards of latitude 620 N and eastwards of longitude 40 W;

.2	the Skagerrak and part of the Kattegat, the southern limit of which is determined east of the Skaw by latitude 57044’ N; and

.3	the English Channel and its approaches eastwards of longitude 50 W and northwards of latitude 48030’ N.

Ballast Water Exchange in the North Sea

8	A ship, on a voyage between 2 ports located in the North Sea, which under the Convention shall at least meet the standard described in regulation D-1, may conduct ballast water exchange in the designated ballast water exchange area in the North Sea. A ship conducting ballast water exchange in this area shall comply with all the regulations for ballast water exchange in the Convention, with the exception of regulation B-4.1.

9	The designated ballast water exchange area in the North Sea is the area with a risk index ARI of less then 0,75, the area which is not red, corrected for the “Kompromisslinie” for the Traffic Separations Scheme Terschelling-German Bright, and corrected for the Norwegian EEZ

10	Within the Norwegian EEZ ballast water exchange areas are displayed in Annex 2.

Annex 1 -  Coordinates of the designated ballast water exchange area in the North Sea

The area with a risk index ARI of less then 0,75, corrected for the “Kompromisslinie” for the Traffic Separations Scheme Terschelling-German

Latitude   Longitude

2	60,66417	0,76472

2	60,59611	0,88750

2	60,50194	0,96083

2	60,41833	0,92139

2	60,33472	1,02611

2	60,18333	1,01833

2	60,05667	1,16611

2	59,85667	1,17250

2	59,85389	1,37611

2	60,01583	1,33972

2	60,19361	1,29528

2	60,13611	1,44944

2	60,21722	1,67167

2	60,32944	1,71333

2	60,35278	1,46250

2	60,37889	1,42500

2	60,48111	1,63500

2	60,68500	1,40250

2	60,63528	1,23250

2	60,82611	1,13583

2	60,84194	1,01306

2	60,95167	0,96583

2	60,95667	0,80389

2	60,84444	0,75167

3	59,22750	2,40667

3	59,06861	2,59222

3	59,13861	2,84556

3	59,34333	3,13639

3	59,35667	2,60000

3	59,32694	2,35639

4	59,15472	3,36278

4	59,14556	3,16833

4	59,15194	3,06250

4	59,06333	2,88861

4	58,91694	2,72056

4	58,80444	2,84611

4	58,69556	2,86667

4	58,71583	2,93250

4	58,76806	3,01639

4	58,75639	3,19222

4	58,76889	3,39889

5	56,86306	-6,91472

5	56,75528	-7,00778

5	56,79278	-6,55889

5	56,90444	-6,55000

6	54,36444	-2,80111

6	54,34056	-2,78194

6	54,36528	-2,69556

6	54,57528	-2,84917

6	54,79556	-2,88750

6	54,92028	-2,97833

6	55,05667	-3,03583

6	55,17889	-3,10778

6	55,31556	-3,16528

6	55,43694	-3,26250

6	55,48083	-3,36639

6	55,59000	-3,51611

6	55,73944	-3,88389

6	55,81722	-4,01639

6	55,70917	-4,39500

6	55,62028	-4,46611

6	55,45306	-4,74167

6	55,39444	-4,66000

6	55,34417	-4,31389

6	55,27000	-4,13778

6	55,13583	-3,97028

6	55,09750	-3,87917

6	54,96333	-3,71139

6	54,92500	-3,62056

6	54,79083	-3,45278

6	54,75250	-3,36167

6	54,57528	-3,15083

6	54,53694	-3,06000

6	54,44583	-2,93528

7	53,93028	-3,36750

7	53,82306	-3,34250

7	53,84333	-2,85028

7	54,18167	-2,77194

7	54,23000	-3,09806

7	54,22167	-3,37111

7	53,99556	-3,35778

8	49,51722	2,41917

8	49,38167	2,47861

8	49,40139	2,71083

8	49,57111	2,50750

9	49,08556	2,05278

9	49,03694	2,09056

9	49,05556	2,20111

9	49,14750	2,23861

9	49,23278	2,29000

9	49,28167	2,11472

9	49,61611	2,05806

9	49,49667	1,94222

9	49,14194	1,98000

10	48,89139	3,31667

10	48,87222	3,08806

10	48,75250	2,93528

10	48,69722	2,78722

10	48,62583	2,73778

10	48,62583	3,91917

10	48,77444	3,91944

10	48,76056	3,88611

10	48,79583	3,57417

10	48,87500	3,51944

10	48,89083	3,44861

10	48,87611	3,38389

11	65,12417	-11,72556

11	54,37611	-11,72917

11	54,40278	-11,52750

11	54,27333	-11,47278

11	54,14750	-11,39889

11	54,09500	-11,21472

11	54,10694	-11,11694

11	54,03722	-11,09750

11	54,02750	-11,24944

11	53,97278	-11,38028

11	54,04861	-11,39972

11	54,06639	-11,49667

11	54,14667	-11,50556

11	54,22944	-11,72917

11	48,62583	-11,73139

11	48,62583	2,59778

11	48,66806	2,49778

11	48,71583	2,41611

11	48,75417	2,28222

11	48,83833	2,13861

11	48,73889	2,05917

11	48,76194	1,87472

11	48,74861	1,76694

11	48,84528	1,72639

11	48,96500	1,65583

11	49,21389	1,68667

11	49,34806	1,85417

11	49,60500	1,90806

11	49,66139	1,98889

11	49,73972	1,91889

11	49,86194	1,90250

11	49,91833	1,75583

11	49,74583	1,68333

11	49,69083	1,42889

11	49,70778	1,29278

11	49,69500	1,18889

11	49,53111	1,20944

11	49,45944	1,13250

11	49,45722	0,96944

11	49,43583	0,79694

11	49,45556	0,63667

11	49,37722	0,22028

11	49,66444	0,00167

11	49,74417	-0,09806

11	49,78889	-0,30500

11	49,92639	-0,53861

11	49,91528	-0,62611

11	49,93694	-0,79861

11	49,94444	-0,98472

11	50,00944	-1,07639

11	50,06333	-1,20472

11	50,36083	-1,26889

11	50,52556	-1,24833

11	50,68333	-1,30917

11	50,74833	-1,08167

11	50,73722	-0,99250

11	50,75778	-0,82833

11	50,69444	-0,60694

11	50,64000	-0,29417

11	50,74250	0,04000

11	50,78083	0,23806

11	50,69444	0,38472

11	50,64500	0,50250

11	50,41833	0,81278

11	50,34611	1,06472

11	50,41028	1,34611

11	50,52694	1,50583

11	50,56528	1,59694

11	50,71667	1,83500

11	50,52194	2,06639

11	50,48361	2,14806

11	50,61306	2,32528

11	50,46722	2,40944

11	50,48833	2,57889

11	50,65611	2,84278

11	50,71778	2,98861

11	50,65139	3,10139

11	50,57500	3,28306

11	50,51194	3,43278

11	50,32361	3,50278

11	50,22028	3,57500

11	50,18194	3,77389

11	50,26806	3,92056

11	50,26833	3,92194

11	53,39583	3,92722

11	53,41111	3,70500

11	53,49361	3,49028

11	53,66972	3,45111

11	53,88722	3,62528

11	54,00417	3,55667

11	54,10139	3,43500

11	54,23972	3,45222

11	54,44583	3,70972

11	54,68139	3,92917

11	58,57444	3,93583

11	58,58694	3,79278

11	58,69167	3,41111

11	58,66806	3,01528

11	58,52306	3,02083

11	58,41139	3,01639

11	58,30944	3,12667

11	58,20056	3,40639

11	58,06139	3,52417

11	57,94167	3,44778

11	57,87472	3,38556

11	57,77000	3,27278

11	57,74333	2,46833

11	57,72694	2,21972

11	57,72694	2,04722

11	57,68417	1,82722

11	57,54083	1,74389

11	57,39861	1,76889

11	57,33556	1,90278

11	57,09694	2,07528

11	56,94861	2,11111

11	56,81472	2,15806

11	56,73444	2,32833

11	56,64167	2,46333

11	56,47417	2,54250

11	56,38639	2,58889

11	56,30250	2,58556

11	56,17389	2,49917

11	56,06750	2,50333

11	55,95833	2,11111

11	55,79667	1,90056

11	55,67278	1,41250

11	55,56500	1,37667

11	55,41444	1,38250

11	55,33889	1,52028

11	55,22583	1,52556

11	55,02444	1,29139

11	54,96583	1,29361

11	54,92250	1,29194

11	54,83667	1,29528

11	54,62250	0,96389

11	54,53528	0,68833

11	54,44583	0,51917

11	54,36278	0,34333

11	54,23361	0,25778

11	54,22944	0,15278

11	54,14278	-0,09472

11	53,82306	-0,08194

11	53,73833	-0,26111

11	53,67139	-0,38806

11	53,62833	-0,61278

11	53,54194	-0,77611

11	53,43528	-1,11278

11	53,32639	-1,16417

11	53,27944	-1,26333

11	53,14528	-1,38778

11	53,02611	-1,64028

11	52,89528	-1,85417

11	52,85361	-1,98500

11	52,80722	-2,11750

11	52,81222	-2,24333

11	52,66056	-2,29139

11	52,47944	-2,28417

11	52,24694	-2,12417

11	51,86028	-2,07139

11	51,46583	-1,95583

11	51,30139	-2,07917

11	51,42861	-2,31972

11	51,51194	-2,66972

11	51,64639	-2,88889

11	51,69306	-2,98806

11	51,81889	-3,10472

11	51,86028	-3,19250

11	52,15361	-3,55306

11	52,24833	-3,79611

11	52,29306	-3,88083

11	52,33472	-4,01167

11	52,49444	-4,24417

11	52,63806	-4,31194

11	52,72278	-4,35667

11	52,89694	-4,39806

11	53,03333	-4,44611

11	53,25333	-4,43722

11	53,42528	-4,25167

11	53,57889	-4,33306

11	53,62806	-4,74472

11	53,67306	-4,82944

11	53,81389	-5,16417

11	53,75028	-5,46750

11	53,76278	-5,78444

11	53,93167	-5,86417

11	54,01333	-5,95222

11	54,08694	-5,94944

11	54,20556	-6,25389

11	54,12333	-6,48861

11	54,03833	-6,93278

11	54,06444	-7,59000

11	54,22250	-7,67528

11	54,46861	-7,48667

11	54,50167	-6,98056

11	54,82222	-6,48639

11	54,92806	-6,34028

11	55,02278	-6,44250

11	55,17500	-6,76472

11	55,55583	-6,81667

11	55,65639	-6,81278

11	55,78917	-6,90417

11	55,77778	-7,19056

11	55,82889	-7,28722

11	55,87028	-7,37500

11	55,91528	-7,45972

11	56,02833	-7,75028

11	56,61611	-7,64306

11	56,88278	-7,96806

11	57,00444	-8,02556

11	57,15639	-8,18972

11	57,21778	-7,93250

11	57,29833	-7,93583

11	57,41333	-8,17972

11	57,25278	-8,94722

11	57,38833	-9,33444

11	57,50917	-9,27056

11	57,59583	-9,27389

11	57,63833	-9,18444

11	57,70861	-9,18722

11	57,76750	-9,32333

11	57,63833	-9,44306

11	57,55361	-9,71139

11	57,64583	-9,88556

11	57,85389	-9,83111

11	58,02139	-9,78972

11	58,07278	-10,11167

11	58,16528	-10,46472

11	58,07111	-10,65194

11	57,89694	-10,95222

11	57,85556	-11,08333

11	57,76139	-11,27250

11	57,59528	-11,42667

11	57,55361	-11,49389

11	57,82222	-11,42361

11	58,02194	-11,43139

11	58,12500	-11,37694

11	58,27389	-11,21639

11	58,46083	-11,12806

11	58,66833	-10,90417

11	58,84722	-10,73833

11	58,88861	-10,69361

11	59,11778	-10,60444

11	59,23444	-10,60889

11	59,27750	-10,60722

11	59,36389	-10,61083

11	59,46278	-10,58861

11	59,53556	-10,45528

11	59,40944	-10,54222

11	59,24583	-10,55306

11	59,08250	-10,48556

11	58,98556	-10,35167

11	58,92028	-10,07778

11	58,91333	-9,86278

11	58,88861	-9,66028

11	58,67306	-9,31528

11	58,52194	-9,02306

11	58,37139	-8,79806

11	58,24194	-8,58222

11	58,20056	-8,36500

11	58,07361	-8,20833

11	58,02194	-8,00111

11	58,03611	-7,64722

11	57,97528	-7,53222

11	57,98833	-7,20167

11	57,98222	-7,05083

11	57,98528	-6,97667

11	58,04111	-6,80806

11	58,04167	-6,53194

11	58,20000	-6,55750

11	58,24194	-6,33861

11	58,28667	-6,25389

11	58,37139	-6,03667

11	58,41611	-5,95222

11	58,45750	-5,77806

11	58,69056	-5,45556

11	58,99472	-5,48583

11	59,06111	-5,61500

11	59,21444	-5,58750

11	59,21583	-5,39639

11	59,08417	-5,22972

11	59,06278	-5,15083

11	59,32639	-5,08972

11	59,38250	-5,10917

11	59,40917	-5,17944

11	59,53611	-5,15111

11	59,60111	-5,19667

11	59,60250	-5,11083

11	59,64278	-5,06833

11	59,80056	-5,04444

11	59,88361	-5,04639

11	60,10361	-5,18472

11	60,18917	-5,21139

11	60,20000	-4,93861

11	60,34278	-4,90222

11	60,40917	-4,97139

11	60,56222	-4,88861

11	60,70167	-4,84306

11	60,88222	-4,93417

11	60,93056	-4,89167

11	61,02306	-4,93111

11	61,02472	-4,72639

11	61,12917	-4,70361

11	61,19306	-4,75222

11	61,22917	-4,95222

11	61,40528	-4,94472

11	61,52500	-5,07194

11	61,53556	-5,02667

11	61,62500	-4,94306

11	61,67250	-4,87250

11	61,87972	-4,70972

11	61,93472	-4,83222

11	61,96333	-5,05278

11	55,78333	-10,26111

11	55,70611	-10,17861

11	55,63417	-10,50028

11	55,71917	-10,47472

11	54,61556	-10,35056

11	54,55611	-10,54333

11	54,81694	-10,57861

11	54,78583	-10,42556

11	54,42194	-7,52222

11	54,22250	-7,67528

11	53,92139	-7,77556

11	53,86056	-7,34167

11	53,93167	-6,50611

11	54,01750	-6,33972

11	54,05972	-6,04750

11	53,74583	-6,28583

11	53,69611	-6,23389

11	53,58750	-5,67889

11	53,58333	-5,46472

11	53,49806	-5,21500

11	53,48500	-5,18611

11	53,46083	-5,07028

11	53,43250	-4,96194

11	53,24917	-4,65861

11	53,18250	-4,58861

11	53,04639	-4,44556

11	53,03333	-4,44611

11	52,92444	-4,40778

Annex 2

The North Sea and Norwegian ballast water exchange areas

# Footnotes

English only

The definition of the North Sea is consistent with MARPOL 73/78, Annex V, Regulation 5 (1) (f), but above that includes a part of the Kattegat so that traffic to and from Gothenburg is included.